## Slide 1: Xampling
Analog-to-digital at Sub-Nyquist rates
Yonina Eldar
Department of Electrical Engineering
Technion – Israel Institute of Technology
http://www.ee.technion.ac.il/people/YoninaEldar/ yonina@ee.technion.ac.il
ISIT Tutorial
July 31st, 2011
Notes: Have a dream come true

## Slide 2: “Analog Girl in a Digital World…”
Voice recorder
Camera
Medical imaging
Analog signal
ADC
Digital domain
Compress ~1:10
De- Compress
DAC
Analog signal
Nyquist rate
Judy Gorman `99
“Can we not just directly measure the part that will not end up being thrown away ?”
Donoho, ‘06

## Slide 3: Key Idea
Reduce storage/reduce sampling rates
Reduce processing rates
Increase imaging resolution
Reduce power, size, cost…
Exploit structure to improve data processing performance:
Goal:
Survey sampling strategies that exploit signal structure to reduce rate
Present a unified framework for sub-Nyquist sampling
Provide a variety of different applications and benefits

## Slide 4: Outline
Part 1: Introduction
Part 2: Sub-Nyquist in a subspace
  Generalized sampling framework
  Examples
Part 3: Union of subspaces
  Model, analog and discrete applications
  Short intro to compressed sensing
Part 4: Xampling, Sub-Nyquist in a union
  Functional framework
  Modulated wideband conversion
  Sparse shift-invariant sampling
  Finite-rate/sequences of innovation methods
  Random demodulation
Part 5: From theory to hardware
  Practical design metrics
  Circuit challenges

## Slide 5: Outline Schematically
Definition: Nyquist-rate system A single ADC device outputs a stream of numbers at rate
Sub-Nyquist system
  One or more ADC devices
  Each ADC device runs at a rate below
  With / without analog preprocessing
High-rate
Low-rate
Overall rate
 Our main focus
Notes: 5

## Slide 6: Tutorial Goal
Feel free to ask questions
Raise ideas
Slow me down if things are too fast …
To be as interactive as possible!
Hope you learn and enjoy!

## Slide 7
– Part 1 –
Introduction
 Outline

## Slide 8
Sampling: “Analog Girl in a Digital World…” Judy Gorman 99
Digital world
Analog world
Reconstruction
D2A
Sampling
A2D
Signal processing
Image denoising
Analysis…
(Interpolation)
Music
Radar
Image…
Very high sampling rates:
hardware excessive solutions
High DSP rates

## Slide 9: ADC Market
State-of-the-art ADCs generate uniform samples at the input’s Nyquist rate
Continuous effort to:
  increase sampling rate (Giga-samples/sec)
  increase front-end bandwidth
  increase (effective) number of bits
Working in digital becomes difficult

## Slide 10
Nyquist Rate Sampling
Standard processing techniques require sampling at the Nyquist rate = twice the highest frequency
Narrow pulse, wide sensing range = high Nyquist rate
Results in hardware excessive solutions and high DSP rates
Too difficult to process, store and transmit
Main Idea:
Exploit structure to reduce sampling and processing rates

## Slide 11: The Key – Structure
piece-wise linear
Sampling reduces ``dimenions’’
Must have some prior on
Sampling
A2D
Uncountable
Countable
bandlimited
Prior (= Signal Model) Necessary for Recovery
Model too narrow (e.g. pure sine)  not widely applicable
Model too wide (e.g. bandlimited)  no rate reduction
Key: Treat signal models that are sufficiently wide and structured at the same time

## Slide 12: Structure Types
In this tutorial we treat 2 main structures:
Subspace
Linear:
Generalized sampling theory
Union of subspaces
Nonlinear:
Xampling (functional framework)
Subspace modeling is used in many practical applications
BUT, can result in unnecessary-high sampling and processing rates
Union modeling paves the way to innovative sampling methods,
at rates as low as the actual information rate

## Slide 13: Ultrasound
Tx pulse
Ultrasonic probe
Rx signal
Unknowns
Echoes result from scattering in the tissue
The image is formed by identifying the scatterers
High sampling rates
High digital processing rates

## Slide 14: Processing Rates
To increase SNR the reflections are viewed by an antenna array
SNR is improved through beamforming by introducing appropriate time shifts to the received signals
Requires high sampling rates and large data processing rates
Subspace: One image trace requires 128 samplers @ 20M, beamforming to 150 points, a total of 6.3x106 sums/frame
Union: can reduce sampling rate by orders of magnitude
Scan Plane
Xdcr
Focusing the received beam by applying delays
Portable Systems
Low-End Systems
High-End Systems
Goal: reduce ultrasound machines to a size of a laptop at same resolution

## Slide 15: Resolution (1): Radar
Principle:
  A known pulse is transmitted
  Reflections from targets are received
  Target’s ranges and velocities are identified
Challenge:
  All processing is done digitally
  Targets can lie on an arbitrary grid
  Process of digitizing  loss of resolution in range-velocity domain
Subspace methods:

## Slide 16: Resolution (2): Subwavelength Imaging
Input
Output
Diffraction limit: Even a perfect optical imaging system has a resolution limit determined by the wavelength λ
  The smallest observable detail is larger than ~ λ/2
  This results in image smearing
Subspace methods:

## Slide 17: Imaging via Union Modeling
Union method
150 nm
Radar:
Subwavelength:
Gazit et al., ‘11
Bajwa et al., ‘11

## Slide 18: Wideband Communication
AM
FM
QPSK
QAM
Subspace methods:
  RF demodulation
  Undersampling
  and more…
Unknown , e.g. cognitive radio. Should we sample at ?
Union modeling:
  Can sample at the actual information bandwidth, even though
  Can process at low rate (no need to reconstruct Nyquist-rate samples)

## Slide 19: Sub-Nyquist Demonstration
FM @ 631.2 MHz
AM @ 807.8 MHz
1.5 MHz
10 kHz
100 kHz
Overlayed sub-Nyquist
aliasing around 6.171 MHz
+
+
FM @ 631.2 MHz
AM @ 807.8 MHz
Sine @ 981.9 MHz
MWC prototype
Carrier frequencies are chosen to create overlayed aliasing at baseband
Reconstruction
(CTF)
Mishali et al., ‘10

## Slide 20: Xampling
Main idea:
  Move compression before ADC
  Use nonlinear algorithms to interface with standard DSP and signal reconstruction
High-rate
Low-rate
SW
HW

## Slide 21: Xampling
SW
HW
New hardware designs
New digital algorithms
Main idea:
  Move compression before ADC
  Use nonlinear algorithms to interface with standard DSP and signal reconstruction
Follow a set of design principles  step from theory to hardware

## Slide 22: From Theory to Hardware
2.4 GHz Nyquist-rate, 120 MHz occupancy
280 MHz sampling rate
49 dB dynamic range
SNDR > 30 dB over input range
Mishali et al., 10
800 kHz Nyquist-rate
100 kHz sampling rate
Ragheb et al., 08
Tutorial briefly covers circuit challenges in sub-Nyquist systems
Sub-Nyquist technology becomes feasible !
Candès et al., 08
Emami et al., 08
RICE 1-pixel camera
DARPA A2I Project
See many more contributors in compressive sensing hardware

## Slide 23: Tutorial Goal
Instead of a single subspace modeling use union of subspaces framework
Adopt a new design methodology – Xampling
Result: Simple hardware and low computational cost on the DSP
Theory, Algorithms, Hardware
  Compression+Sampling = Xampling
X prefix for compression, e.g. DivX
What’s next:
Part 2: Sub-Nyquist in a subspace
Parts 3-5: Sub-Nyquist in union models
Notes: This slide should appear after the current 18 (i.e. write before part II).

## Slide 24
– Part 2 –
Sub-Nyquist in a Subspace
 Outline

## Slide 25: Shannon-Nyquist Sampling
Theorem [Bandlimited Sampling]
Shannon, ‘49
Model: Bandlimited signals
Sampling: Pointwise at rate
Reconstruction: Interpolation by

## Slide 26: Avoiding High-Rate ADC
Use several samplers:
  Papoulis’ theorem
  Time-interleaved ADC (special case)
Exploit signal structure (subspace):
  Pulse streams
  Multiband sampling

## Slide 27: Papoulis’ Theorem
Model: bandlimited (same)
Sampling: branches sampled at the Nyquist rate, Flexible constraints on
Overall rate is (same)
Papoulis, ‘77
Reconstruction:

## Slide 28: Papoulis’ Theorem
Condition on filters: The matrix B has to be invertible over
Recovery filters:

## Slide 29: Example: Derivative Sampling

## Slide 30: Time-Interleaved ADCs
A high-rate ADC comprised of a bank of lowrate devices
Each branch (coset) undersamples at of the Nyquist-rate
Analog Devices Corp.
Texas Instruments Corp.
MAXIM Corp.
National InstrumentsCorp.
Widely-researched
Yen ’56, Eldar and Oppenheim ’00, Johansson and Lowenborg ’02,
Levy and Hurst ’04, and more…
Notes: High rate samplers consist of several low rate ones because we cannot have one at high rate (quantization time)
We need to duplicate the T/H, and the quantizer.
This is a hybrid design – T/H with high BW but quantizer with low rate…. We can’t use low BW T/H, since we need *pointwise* samples of the wideband input

## Slide 31: Practical ADC Devices
In time-interleaved architectures:
The overall rate is Nyquist
Each branch needs front-end with Nyquist bandwidth (will be important later)
Accurate time delay are required
Black and Hodges, ‘80
Jenq, ‘90
Elbornsson et al., ‘05
Divi and Wornell, ‘09
Murmann et al., ‘09
Goodman et al., ’09
…and more

## Slide 32: Generalized Sampling in a Subspace
Model: Shift-invariant (SI) subspace of possible inputs
Practical ! e.g., splines, pulse amplitude modulation (PAM), and more…
Splines: central B-spline

## Slide 33
Generalized anti-aliasing filter
Non-Pointwise Linear Sampling
Sampling functions
Electrical circuit
Local averaging
Sampling space:

## Slide 34: Main Tool: Fourier Transforms
All manipulations in SI spaces can be carried out in Fourier domain!
Continuous time FT:
Discrete time FT: - periodic
DTFT of sampled sequence :
If is used to create :

## Slide 35: Correlation Sequences
Samples can be written as
In the Fourier domain:
The set is orthonormal if
samples

## Slide 36: Reconstruction from Generalized Samples
  Recovery: Filter by to obtain , then interpolate
  Model:
  Sampling:
Shift-invariant case
Sampling rate is rather than the Nyquist rate of
Approach does not depend on
Aldroubi and Unser, ‘94
Christensen and Eldar, ‘05

## Slide 37: Multiple Shift-Invariant Generators
Sampling rate is  independent of
Model:
Sampling / Reconstruction:
Previous work extends theory to arbitrary subspaces
Many beautiful results, and many contributors
(Unser, Aldroubi, Vaidyanathan,Blu, Jerri, Vetterli, Grochenig, DeVore,Christensen,Schoenberg,Eldar …)
More information:
Y. C. Eldar and T. Michaeli, “Beyond Bandlimited Sampling,” IEEE Signal Proc. Magazine, 26(3): 48-68, May 2009
de Boor, DeVore and Ron , ‘94
Christensen and Eldar, ‘05

## Slide 38: Toy-Example (1)
Sampling: choose 3 adjacent shifts contributes to each sample
Recovery: exploit known shape
can be very high, since is not bandlimited
Model:
1
Rate:
Subspace prior

## Slide 39: Toy-Example (2)
Model:
Perfect recovery !
is high…
Rate:
Lowpass data can contain all relevant information !
Notes: 39

## Slide 40: Pulse-streams (known locations)
is high, since is not bandlimited
Sampling: design and sample are known
Model: fixed delays , unknown
Recovery: satisfy a linear system, with coefficients depending on
Rate:
Notes: We focus on 1-d continuous inputs x(t), and particularly multiband frequency supports
A common practice in acquisition of RF signals is undersampling or demodulation

## Slide 41: Generalized Sampling in Practice
So far:
Toy-examples: perfect recovery of nonbandlimited inputs !
Pulse streams, known pulse shape and fixed delays
Sampling & processing rates
A common denominator
exact knowledge
Approach minimal
Design assumption
High
Next slides: Multiband signals, known carrier frequencies

## Slide 42: Mutliband (known carriers)
AM
FM
QPSK
QAM
Model: narrowband transmissions in wideband range, modulated on carrier frequencies
Sampling:
  RF demodulation
  Undesampling
  Nonuniform strategies
Utilize knowledge
Sampling and processing at rate are often impractical
Notes: We focus on 1-d continuous inputs x(t), and particularly multiband frequency supports
A common practice in acquisition of RF signals is undersampling or demodulation

## Slide 43: Landau’s Theorem
Average sampling rate
Theorem (known spectral support)
Landau, ‘67
bands, individual widths , requires at least samples/sec
Note:  bandpass with single-side width requires samples/sec
 transmissions result in bands (conjugate symmetry)
States the minimal sampling rate for any (pointwise) sampling strategy that utilizes frequency support knowledge

## Slide 44: RF Demodulation
AM
FM
QPSK
QAM
value is used in sampling and reconstruction
Analog preprocessing with RF devices (1 branch/transmission)
Minimal rate:
Zero-IF, low-IF topologies
Lowpass
DSP
Interp.
Crols and Steyaert, ‘98
Notes: We focus on 1-d continuous inputs x(t), and particularly multiband frequency supports
A common practice in acquisition of RF signals is undersampling or demodulation

## Slide 45: Undersampling
a.k.a. bandpass sampling
QPSK
DSP
Interp.
Sampling: Select rate to satisfy ``alias free condition’’
Reconstruction: Same as in RF demodulation
No analog preprocessing
Notes: The method suits a single transmission (bandpass), and the rate depends on the band positioning (to avoid self-aliasing)
We can achieve the minimal rate only in integer positioning
No analog hardware (exploits aliasing) but suits only a bandpass input because of the alias-free condition
As we will see in the sequel, it is not precisely true that this is below Nyquist, because the ADC needs Nyquist-rate front-end, but for now we can refer to this as no analog preprocessing

## Slide 46: Allowed Undersampling Rates
Vaughan et al., ‘91
Sampling rate must be chosen in accordance to band location:
Allowed
Forbidden
Robustness to model mismatch requires significant rate increase
Multiband alias-free conditions are complicated and generally do not result in significant rate reduction
~150% increase
above optimal

## Slide 47: Periodic Nonuniform Sampling
Advantages:
  No analog preprocessing
  No ``alias-free’’ conditions, works for multiband
  Approach minimal rate
Sampling:
In general, a p’th-order PNS can resolve up to p aliases:
  Bandpass sampling at average rate 2B
  Multiband sampling at rate approaching minimal
Kohlenberg, ‘53
Lin and Vaidyanathan, ‘98
Notes: In the drawing, for bandpass, 2 overlaps get different weigthing in the 2 branches so that we can resolve them out
We will elaborate on that more when we describe our first sampling strategy which also relies on nonuniform sampling
The choice of phi_i depends on the band positions (in order to create linear independent mixtures). The recosntruction filters have piecewise constant responses, which depends on both band positions and choice of delays

## Slide 48: Reconstruction from 2nd order PNS
Delays result in different linear combinations of the bands

## Slide 49: Multi-Coset Sampling
PNS with delays on the Nyquist grid
Analog signal
Point-wise samples
0
2
3
0
0
2
2
3
3
Samples can be written as where contains the non-zero
bands and
Notes: They sit on the same platform (e.g. receiver) so no real advantage for semi-blind

## Slide 50: Multi-Coset Sampling
PNS with delays on the Nyquist grid
Semi-blind approaches:
  Choose universally (or at random)
  Design reconstruction filters
Herley et. al., ‘99
Bresler et al., ‘00
``Blind’’ recovery:
Bresler et al., ‘96,'98
Positions are implicitly assumed:
  depends on band positions
  Recovery fails if incorrect value is used for
  Result requires random signal model, and holds almost surely
Completely blind = Unknown carriers = not a subspace model !
Notes: They sit on the same platform (e.g. receiver) so no real advantage for semi-blind

## Slide 51: Short Summary
Subspace models
  Linear, easy to treat mathematically
  Not necessarily bandlimited
Generalized sampling theory
  Treat arbitrary subspace models
  Many classic approaches can be derived from theory
  Rate is proportional to actual information rate rather than Nyquist
But, what if…
the input model is not linear ? (for example, when carrier frequencies or times of arrivals are unknown)
Answer: the rest of this tutorial

## Slide 52: Nonlinear Models – Motivation
Encountered in practical applications:
  Cognitive radio mobiles utilize unused spectrum ``holes’’, spectral map is unknown a-priori

## Slide 53: Nonlinear Models – Motivation
Encountered in practical applications:
  Cognitive radio mobiles utilize unused spectrum ``holes’’, spectral map is unknown a-priori
  Ultrasound, reflections are intercepted at unknown delays
Ultrasonic probe
Rx signal
Unknowns
Do not fit subspace modeling … we can always sample at rate
Questions:
  Better modeling? Subspace up to some uncertainty ?
  Can we sample and process at rates below with proper modeling?

## Slide 54
– Part 3 –
Union of Subspaces
 Outline

## Slide 55: Model
Signal belongs to one out of (possibly infinitely-)many subspaces
Each corresponds to a different subspace
belongs to , for some  But, is unknown a-priori
is a nonlinear model:
A union is generally a true subset of its affine hull:
Lu and Do, ‘08
Eldar and Mishali, ‘09
The union tells us more about the signal!

## Slide 56: Union Types
4 types:
Legend:
  = General analog union models Infiniteness enters in either
  = Discrete models, e.g., sparse trigonometric polynomials

## Slide 57: Examples: Analog Unions (1)
Dimensions:
Pulses with unknown time delays
A special case of a broader model: finite rate of innovation (FRI) Here, innovation rate =
Sequences of innovation model has both dimensions infinite
Vetterli et al., ’02-’11
Gedalyahu and Eldar, ’09-’11

## Slide 58: Examples: Analog Unions (2)
Multiband with unknown carrier frequencies
Dimensions:
Another viewpoint with is described later on (efficient hardware and software implementation)
Mishali and Eldar ’07-’11

## Slide 59: Examples: Discrete Unions
Signal model has underlying finite parameterization
Tropp et al., ’09
Continuous-time examples:
  Sparse trigonometric polynomials
  Sparse piece-wise constant with integer knots
Discrete-time examples:
  Compressed sensing
  Block sparsity, tree-sparse models
Donoho, Candès-Romberg-Tao, ‘06
Baraniuk et al., Eldar et al., ’09-’11
Kunis and Rauhut, ’08

## Slide 60: Compressed Sensing = Union
Each is a subspace
- sparse
Denoising and deblurring
Tracking and classification
Compressed sensing
Sparsity models have been used successfully in many applications such as:
Donoho, Johnstone, Mallat, Sapiro, Ma, Vidal, Starck, …
Candès, Romberg, and Tao ‘06
Donoho ‘06

## Slide 61: Compressed Sensing
For sub-Nyquist sampling, our focus is on infinite unions
We will start with compressed sensing (CS)
  easier to explain
  methods for infinite unions also rely on CS algorithms
Following a short intro on CS  Xampling and analog systems
CS

## Slide 62: Short Intro
Compressed 148 KB 6%
Original 2500 KB 100%
“Can we not just directly measure the part that will not end up being thrown away ?”
Donoho, ‘06

## Slide 63: In a Nutshell…
Donoho, ‘06
Candès-Romberg-Tao, ‘06
Notes: 63

## Slide 64: Uniqueness of Sparse Representations
How many samples are needed to ensure uniqueness?
V
V
V
V
v
Problem: Condition hard to verify
Notes: 64

## Slide 65: Coherence
The coherence of A is defined by (assuming normalized columns)
Welch bound:
When
Uniqueness of y=Ax can be expressed in terms of as
Under same condition we will see that efficient recovery is possible as well
Donoho et al., ‘01
Tropp, ‘04
Notes: 65

## Slide 66: Restricted Isometry Property (RIP)
When noise is present uniqueness cannot be guaranteed
Would like to ensure stability
Can be guaranteed using RIP
A has RIP of order if
for any k–sparse vector x
In this case A is an approximate isometry
If A has unit-columns and coherenc then it has the RIP with
Candès and Tao, ‘05
Notes: 66

## Slide 67: Recovery of Sparse Vectors
Find the sparsest and consistent
Alternative recovery algorithms (Polynomial-time):
NP-Hard !!
Basis pursuit
Convex and tractable
Greedy algorithms
OMP, FOCUSS, etc.
Reconstruction:
Donoho, ‘06
Candès et al., ‘06
Candès, ‘08
Donoho and Elad, ‘03
Tropp, Elad, Cotter et al.,
Chen et al., and many others…
Notes: 67

## Slide 68: Greedy Methods: Matching Pursuit
Essential algorithm:
  Choose the first “active” column (maximally correlated with )
  Subtract off to form a residual
  Repeat with
Very fast for small scale problems
Not as accurate/robust for large signals in the presence of noise
Orthogonal MP:
Improve residual computation
Mallat and Zhang, ‘93
Pati et al., ‘93
Notes: 68

## Slide 69: Recovery In the Presence of Noise
-relaxation techniques (convex optimization problems)
  Basis pursuit denoising (BPDN) / Lasso:
  Dantzig selector:
Greedy approaches: stop when data error is on the order of the noise
Candès and Tao, ‘07
Tibshirani ‘96
Chen et al., ‘98
Notes: 69

## Slide 70: Recovery Gurantees
Common settings:
Random sensing matrix A, random noise
  RIP (and similar properties) can be approximated w.h.p.
  RIP-based guarantees for Dantzig selector and BPDN:
Deterministic A and x, random
  RIP typically unknown, coherence must be used
  Coherence-based results for BPDN, OMP, thresholding:
Deterministic “adversarial” noise w:
  Guarantees on order of
Candès and Tao, ’07
Bicket et al., 09
Ben-Haim, Eldar and Elad, ’10
Donoho et al., ’06

## Slide 71: The Sensing Matrix A
Random IID matrices ensure recovery with high probability for sub-Gaussian distributions (Gaussian, Rademacher , Bernoulli, bounded RVs …) when
Random partial Fourier matrices (or more generally unitary matrices) also ensure recovery with a slightly higher number of measurements
Some structured matrices work as well such as a Vandermonde matrix
Tutorials on Compressed Sensing:
R. G. Baraniuk, “Compressive sensing,” IEEE Signal Processing Mag., 24(4), 118–124, July 2007.
E. J. Candès and M. B. Wakin, “An introduction to compressive sampling,” IEEE Sig. Proc. Mag., 25(3), 21–30, Mar. 2008.
M. Duarte and Y. C. Eldar, “Structured Compressed Sensing: From Theory to Applications,” TSP.
Y. C. Eldar and G. Kutyniok, “Compressed Sensing: Theory and Applications,” Cambridge Press.
Donoho, ‘06
Candès et al., ‘06
Notes: 71

## Slide 72
Sub-Nyquist in a Union
  High-sampling rate
  Analog bandwidth issues
  Load on the digital processing due to the excessive rate
Imposing subspace model is inefficient, problems
Generalized sampling theory for unions?
Still developing…
Apply CS on discretized analog models?
…at the price of model sensitivity, high computational loads, and loss of resolution
Rule of thumb: 1 MHz Nyquist = CS with 1 Million unknowns !

## Slide 73: Multiband: Discretization ?
Instead of analog multiband:
Work with discrete multi-tone:
Model size:
Problems:
Advantages:
Proportional to actual bandwidth
Proportional to Nyquist rate
Mishali, Eldar and Elron, ‘10

## Slide 74: Multiband: Discretization ?
Instead of analog multiband:
Work with discrete multi-tone:
Model size:
Problems:
Advantages:
Sensitivity:
System “grid” must match signal tones grid
0.005% grid mismatch
Negligible (for a slight rate increase)
Cannot avoid grid mismatch
huge-scale
Mishali, Eldar and Elron, ‘10

## Slide 75: Multiband: Discretization ?
Instead of analog multiband:
Work with discrete multi-tone:
Model size:
Problems:
Advantages:
Sensitivity: Negligible
System “grid” must match the unknown signal tones grid
Computational load (100 MHz processer):
Realtime processing
Analog
Discretization ?
Mishali, Eldar and Elron, ‘10

## Slide 76: Discrete CS Radar
A discrete version of the channel is being estimated
Leakage effect  fake targets
Limited resolution to
Sampling process in hardware is unclear
Digital processing is complex and expensive
Leakage effect  fake targets
Real channel
Discretized channel
Bajwa, Gedalyahu and Eldar, ’11
Notes: Moshiko: add ref to the graphs

## Slide 77: ADCs: Why Not Standard CS?
CS is for finite dimensional models (y=Ax)
Loss in resolution when discretizing
Sensitivity to grid, analog bandwidth issues
Is not able to exploit structure in analog signals
Results in large computation on the digital side
Samples do not typically interface with standard processing methods
More elaborate signal models needed that exploit structure to reduce sampling and processing rates

## Slide 78
Sub-Nyquist in a Union
Imposing subspace model is inefficient, problems
Generalized sampling theory for unions?
Still developing…
Apply CS on discretized analog models?
Discretization issues…
Must combine ideas from Sampling theory and CS recovery algorithms

## Slide 79
– Part 4 –
Xampling
 Outline
  CS+Sampling = Xampling
X prefix for compression, e.g. DivX
Functional approach to sub-Nyquist in a Union

## Slide 80: Standard DSP Systems
High-rate
Low-rate
Sampling and processing at high rates = Nyquist of
After compression, data has low rate
Standard DSP software expects Nyquist-rate samples rely on invariant properties (enables digital filtering / digital estimation for example)
Move compression to hardware before ADC !
SW
HW

## Slide 81: Xampling – Architecture
Functional architecture: Both sampling and processing at low rate
 Detection block outputs lowrate data that DSP can handle
Built bottom-up: based on practical and pragmatic considerations
Mishali, Eldar and Elron, ‘10
Low-rate
Low-rate
Low-rate
Notes: We call X-ADC… X-DSP… and as we shall see CS and other methods get into the play in the detection stage.

## Slide 82: Xampling: Main Idea
Principle #1 (X-ADC):
Create several streams of data
Each stream is sampled at a low rate
(overall rate much smaller than the Nyquist rate)
Each stream contains a combination from different subspaces
New hardware design ideas
New DSP algorithms
Principle #2 (X-DSP):
Identify subspaces involved (e.g., using CS)
Recover using standard sampling results

## Slide 83
Xampling Systems
Eldar, ‘09
Vetterli et al., ’02-’07
Dragotti et al., ’02-’07
Gedalyahu, Tur and Eldar, ’10-’11
Tropp et al., ’09
Modulated wideband converter
Periodic nonuniform sampling (fully-blind)
Sparse shift-invariant framework
Finite rate of innovation sampling
Random demodulation
Mishali and Eldar, ‘07-’09
Mishali and Eldar, ‘07-’09

## Slide 84
no more than N bands, max width B, bandlimited to
Each band has an uncountable number of non-zero elements
Band locations lie on the continuum
Band locations are unknown in advance
Multiband Union
~
~
~
~
Mishali and Eldar, ‘07
Notes: 84
84

## Slide 85
Optimal Blind Sampling Rate
Average sampling rate
Theorem (known spectral support)
Theorem (unknown spectral support)
The minimal rate is doubled
bands, individual widths , requires at least samples/sec
Mishali and Eldar, ‘07
Landau, ‘67

## Slide 86: The Modulated Wideband Converter
~
~
~
~
Mishali and Eldar, ’09
Notes: 86

## Slide 87: Recovery From Xamples
~
~
~
~
Cannot invert a fat matrix!
Spectrum sparsity: Most of the are identically zero
For each n we have a small size CS problem
Problem: CS algorithms for each n  many computations
Notes: 87

## Slide 88: Reconstruction Approach
Solve finite problem
Reconstruct
0
1
2
3
4
5
6
S = non-zero rows
CTF
(Support recovery)
Continuous
Finite
The matrix V is any basis for the span of
Notes: 88

## Slide 89: Underlying Theory
Theorem [Exact Support Recovery, CTF]
Mishali and Eldar, ‘08
CTF = Continuous to Finite
Construct a frame
for
Solve MMV

## Slide 90: Insight into CTF
nonlinear
Construct frame
Solve CS system
Apply on for each time-instance
Computationally heavy
Computationally light
easy
nonlinear
linear
Run CS recovery
for each time-instance

## Slide 91: Reconstruction
Memory
CTF
(Support recovery)
DSP
(Baseband)
Analog
Back-end
(Realtime)
High-level architecture
Detector
Recover any desired spectrum slice at baseband
Mishali and Eldar, ‘07-’10

## Slide 92: Reconstruction
Memory
CTF
(Support recovery)
DSP
(Baseband)
Analog
Back-end
(Realtime)
High-level architecture
Detector
Mishali and Eldar, ‘07-’10

## Slide 93: Reconstruction
Memory
CTF
(Support recovery)
DSP
(Baseband)
Analog
Back-end
(Realtime)
High-level architecture
Detector
Can reconstruct:
The original analog input exactly (without noise)
Improve SNR for noisy inputs, due to rejection of out-of-band noise
Any band of interest, modulated on any desired carrier frequency
Mishali and Eldar, ‘07-’10

## Slide 94: Sign-Flipping Periodic Waveforms
rectangular (signs)
square (DFT)
Theorem [Expected-RIP for MWC]
Mishali and Eldar, ‘09
ExRIP – RIP holds
with probability p

## Slide 95: Time Appearance of Mixing Waveforms
Bad news: can’t design nice sign patterns at GHz rates
Good news: only the periodicity matters !
Competing approaches (pure CS) struggle with time appearance

## Slide 96: Simulation
~
~
~
~
Notes: 96

## Slide 97: Sub-Nyquist Demonstration
FM @ 631.2 MHz
AM @ 807.8 MHz
1.5 MHz
10 kHz
100 kHz
Overlayed sub-Nyquist
aliasing around 6.171 MHz
+
+
FM @ 631.2 MHz
AM @ 807.8 MHz
Sine @ 981.9 MHz
MWC prototype
Carrier frequencies are chosen to create overlayed aliasing at baseband
Reconstruction
(CTF)
Mishali et al., ‘10

## Slide 98
Xampling Systems
Eldar, ‘09
Vetterli et al., ’02-’07
Dragotti et al., ’02-’07
Gedalyahu, Tur and Eldar, ’10-’11
Tropp et al., ’09
Modulated wideband converter
Periodic nonuniform sampling (fully-blind)
Sparse shift-invariant framework
Finite rate of innovation sampling
Random demodulation
Mishali and Eldar, ‘07-’09
Mishali and Eldar, ‘07-’09

## Slide 99: Fully-Blind PNS Approach
~
~
~
~
Mishali and Eldar, ‘07

## Slide 100: Can Avoid RF Front-end ?
?
=
YES ! If the input bandwidth is not too high…

## Slide 101: Practical ADC Devices
In non-uniform sampling:
Both T/H and mux operate at the Nyquist rate
Digital processing and recovery requires interpolation to the high Nyquist grid
Accurate time-delays are needed

## Slide 102
Xampling Systems
Eldar, ‘09
Vetterli et al., ’02-’07
Dragotti et al., ’02-’07
Gedalyahu, Tur and Eldar, ’10-’11
Tropp et al., ’09
Modulated wideband converter
Periodic nonuniform sampling (fully-blind)
Sparse shift-invariant framework
Finite rate of innovation sampling
Random demodulation
Mishali and Eldar, ‘07-’09
Mishali and Eldar, ‘07-’09

## Slide 103
Sparse Shift-Invariant Framework
Sampling signals from a structured union of shift-invariant spaces (SI)
There is no prior knowledge on the exact indices in the sum
Reconstruction
CTF
Real-time
processing
Theorem
“Good” CS matrix
Sampling theory
Sampling kernels
Reconstruction kernels
Eldar, ‘09

## Slide 104
Xampling Systems
Eldar, ‘09
Vetterli et al., ’02-’07
Dragotti et al., ’02-’07
Gedalyahu, Tur and Eldar, ’10-’11
Tropp et al., ’09
Modulated wideband converter
Periodic nonuniform sampling (fully-blind)
Sparse shift-invariant framework
Finite rate of innovation sampling
Random demodulation
Mishali and Eldar, ‘07-’09
Mishali and Eldar, ‘07-’09

## Slide 105: Pulse Streams
Delays and amplitudes are unknown
Applications:
  Communication
  Radar
  Bioimaging
  Neuronal signals
Special case of Finite Rate of Innovation (FRI) signals
Minimal sampling rate – the rate of innovation:
degrees of freedom per unit time
Vetterli et al., ’02

## Slide 106: Analog Sampling Stage
Naïve attempt: direct sampling at low rate
Most samples do not contain information!!
Sampling rate reduction requires proper design of the analog front-end
Periodic pulse streams
Finite
Infinite pulse streams
Special cases:
Vetterli et al., ’02-’05
Dragotti et al., ’07-’10
Tur et al., ’10-’11
Gedalyahu et al., ’09

## Slide 107: Periodic Pulse Streams
Periodic FRI signal model:
  The function h(t) and the period are known
Since x(t) is periodic it has a Fourier series with coefficients
Spectral estimation: sum of complex exponentials problem
Solved using 2L measurements
  Methods: annihilating filter, MUSIC, ESPRIT
Vetterli et al., ’02-’05
Once the Fourier coefficients are known,
Standard solutions exist.
Challenge: How can we obtain the coefficients?
Stoica and Moses, ’97
Roy and Kailath, ’89
Schmidt, ’86
Notes: The basis for both approaches lies within the framework of spectral estimation. In order to understand this relationship
We begin by observing the periodic FRI model.
We assume a tau-periodic signal of the form depicted here above. The pulse shape is known, and the goal is to recover L delays and amplitudes of its occurrences.

## Slide 108: General Approach
Analog domain
Digital domain
Find Fourier Coefficiens
Sub-Nyquist
Annihilating filter, MUSIC, ESPRIT…
“Mixing” filter
Spectral Estimation
Samples linear combinations of the Fourier coefficients
Identify signal
subspace
(= X-DSP)
Notes: In the analog domain, the FRI signal is filtered with the compactly supported kernel s*(-t) and then sample at interval T, such that N>=2L samples are obtained uniformly within the interval [0,tau).
The filtering and sampling block results in a set of samples, c[n], such that each sample represents some mixture of the signal’s Fourier coefficients. Here we still regard the input signal as periodic.
As we soon show, proper selection of the kernel results in samples which are mixture of the required set of coefficients only. Furthermore, the mixing operator is invertible, such that we may retrieve the coefficients via Digital processing.
The next step involves spectral estimation for extracting the set of delays. Least square method is finally utilized for retrieving the corresponding amplitudes.
(I have added the inverse of S to the equation x=pinv(V)c)

## Slide 109
Find Fourier Coefficients
Find Fourier Coefficiens
Fourier series of a periodic input:
Unknown
Sensing with lowpass:
Known measurements

## Slide 110: Annihilating ``Filter’’
Goal: design a digital filter with
has zeros at the ``frequencies’’ annihilates
Filter coefficients can be computed from the measurements:
Notes: In the analog domain, the FRI signal is filtered with the compactly supported kernel s*(-t) and then sample at interval T, such that N>=2L samples are obtained uniformly within the interval [0,tau).
The filtering and sampling block results in a set of samples, c[n], such that each sample represents some mixture of the signal’s Fourier coefficients. Here we still regard the input signal as periodic.
As we soon show, proper selection of the kernel results in samples which are mixture of the required set of coefficients only. Furthermore, the mixing operator is invertible, such that we may retrieve the coefficients via Digital processing.
The next step involves spectral estimation for extracting the set of delays. Least square method is finally utilized for retrieving the corresponding amplitudes.
(I have added the inverse of S to the equation x=pinv(V)c)

## Slide 111: X-ADC: Filter Choice
Theorem [Sufficient Condition]
Tur, Eldar and Friedman, ’11
Notes: We now summarize the sufficient condition which the filter s(t) must satisfy, so that we may retrieve the set Kappa of Fourier coefficients from the samples c[n]

## Slide 112: Special Cases
Low pass filter
Sum of sincs (SoS) in the frequency domain
In the time domain
Compact support!
Tur, Eldar and Friedman, ’11
Vetterli et al., ’02

## Slide 113: Finite Pulse Streams
SoS filter can be used for finite streams due to its finite support!
Not true for LPF or other filters with long support
Far more robust than
Spline based methods –
works even for high L!

## Slide 114: Multichannel Scheme
Proposed scheme:
Mix & integrate
Take linear combinations
from which Fourier coeff.
can be obtained
Supports general pulse shapes (time limited)
Operates at the rate of innovation
Stable in the presence of noise
Practical implementation based on the MWC
Single pulse generator can be used
Fourier coeff. vector
Samples
Gedalyahu, Tur and Eldar, ’11

## Slide 115: Filter Bank Approach
Serial-to-Parallel
The analog sampling filter “smoothens” the input signal :
  Allows sampling of short-length pulses at low rate
  CS interpretation: each sample is a linear combination of the signal’s values.
The digital correction filter-bank:
  Removes the pulse and sampling kernel effects
  Samples at its output satisfy:
  The delays can be recovered using ESPRIT as long as
Gedalyahu and Eldar, ’09

## Slide 116: Filter Bank vs. Single Filter \ Modulation Bank
FRI models can be treated with both a FB structure or a single filter\modulation bank
Comparison:
FB MB
Model fixed delay in different periods varying delays
arbitrary time support support within one
period
Correction digital correction simple correction
with filter bank

## Slide 117: Noise Robustness
L=2 pulses, 5 samples
L=10 pulses, 21 samples
MSE of the delays estimation, versus integrators approach
The proposed scheme is stable even for high rates of innovation!
Kusuma and Goyal, ’06

## Slide 118: Application: Multipath Medium Identification
LTV channel
propagation paths
Medium identification:
  Recovery of the time delays
  Recovery of time-variant gain coefficients
pulses per period
The proposed method can recover the channel parameters from sub-Nyquist samples
Gedalyahu and Eldar, ’09-’10

## Slide 119: Application: Radar
Each target is defined by:
  Range – delay
  Velocity – doppler
Targets can be identified with infinite resolution as long as the time-bandwidth product satisfies
Bajwa, Gedalyahu and Eldar, ’11

## Slide 120: Xampling in Ultrasound Imaging
Motivation
  Generate a two-dimensional focused ultrasound image while reducing the sampling rate in each active element far below the Nyquist rate
  Sample rate reduction leads to significant reduction of data size, and implies potential reduction of machinery size and power consumption, while maintaining image quality
Portable Systems
Low-End Systems
Mid-Range Systems
High-End Systems
Reduction of sampling rate implies potential reduction of machinery size and power consumption
Wagner, Eldar, Feuer, Danin and Friedman, ’11

## Slide 121: Xampling in Ultrasound Imaging
Main Results
  A scheme which enables reconstruction of a two dimensional image, from samples obtained at a rate 10-15 times below Nyquist
  The resulting image depicts strong perturbations in the tissue
Xampled B-mode image, generated from samples obtained at 0.17 Nyquist Rate
Standard B-mode image, generated from samples obtained at Nyquist Rate

## Slide 122: Ultrasound Imaging & FRI
  - Individual traces of reflected echoes, received by the multi-element transducer array
Can we stably reconstruct pulse streams from low-rate samples?
  An ultrasonic pulse is transmitted into a tissue; echoes are scattered and reflected by density and propagation-velocity perturbations
Beamformed Signal
Digital Beamformer
Meets the finite FRI model:
Unknowns
Notes: Towards conclusion, we would like to tie our results to ultrasound imaging.
We regard a typical B-mode scan, in which a planar cross section of the tissue is rendered.
An imaging cycle begins when a focused ultrasonic pulse is transmitted into the tissue by an array of transducer elements. The same array then receives echoes of the transmitted pulse, which are reflected by density and propagation-velocity perturbations inside the tissue.
In standard imaging devices, the received signals are now sampled at high rate (typically 20MHz per element) as dictated by Nyquist theorem.
The sampled signals are digitally combined with appropriate, time-varying delays, by a beamformer unit, resulting in a focused beam which corresponds to the perturbations along the path of the transmitted pulse.
We observe that the signal received in each element typically comprises streams of pulses originating in macroscopic perturbations, accompanied by noisy-like speckles, originating in microscopic perturbations. We may thus imply the finite FRI model onto the signal received by each element, where our goal is to recover the time-delays and amplitudes of relatively strong echoes.

## Slide 123
Phantom comprising 5 equally spaced scatterers
Real data acquired by GE Healthcare’s Vivid-i imaging system
Method applied on noisy signal
Excellent reconstruction from sub-Nyquist samples
Poor SNR motivates integration of the data from multiple receivers
  How should we combine the information from all channels in the compressed domain?
Ultrasound Experiment
Notes: In the following ultrasound experiment we used our Multi-Channel sampling scheme in order to sample an actual signal which was detected by a single transducer element.
The data was acquired by a GE Healthcare’s Vivid-i imaging system, in a setup comprising five scattering elements.
In this scenario, sampling the signal at Nyquist rate results in approximately 4000 samples per interval tau. Our reconstruction, on the other hand, is based on N=17 samples only. We manage to obtain good estimation of the significant transients, despite the speckle noise.
Nevertheless, the poor SNR and the need to combine multiple 1D signals into a single 2D image, motivates us to integrate data from multiple receivers.
123

## Slide 124: Beamforming in the Compressed Domain
Beamformed signal
Distortion, m
Conceptual beamforming
1D Xampling
Distortion, m
Distortion, -M
Distortion, M
Wagner, Eldar, Feuer, Danin and Friedman, ’11
Notes: Here we present a preliminary approach, of which details are beyond the scope of the current session.
The idea is to modify the modulating kernels applied in the multi-branch scheme, such that the resulting samples are invariant to the offset of the transducer element relative to the constructed beam. In such manner the received signals may be combined for SNR reduction and for obtaining a signal which may be translated to an actual image line.
The slide illustrates the main concept:
We begin with a scheme in which a beam is “conceptually” formed from received signals in the analog domain and then injected into the multichannel Xampling block.
We end with a scheme in which the required signal distortions are translated into modifying the modulating kernels, such that the Xampling block once

## Slide 125: Beamforming in the Compressed Domain
1D Xampling
Distortion, m
Distortion, m
Samples from the rest of the active elements
Samples from the rest of the active elements
Standard Imaging
Xampled Image, Dynamic Focusing with
L = 30; ρ = 3.
RF ultrasound data provided by Dr. Omer Oralkan and Prof. Pierre Khuri-Yakub of the E. L. Ginzton Laboratory at Stanford University.
Wagner, Eldar, Feuer, Danin and Friedman, ’11
Notes: We end with a scheme in which the required signal distortions are translated into modification of the modulating kernels, such that the Xampling block is once again applied to the actual analog input.
The left image was generated via standard sampling and beam-forming techniques, whereas the right image was obtained with about 1/5 the number of samples, by assuming 30 reflecting elements along a single image line, and with factor 3 oversampling.

## Slide 126: Application to GPS Acquisition
  Goal: reducing complexity in GPS acquisition by using fewer correlators
  Signal model:
Li, Rueetschi, Eldar and Scaglione, ’11
satellite code

## Slide 127: Received Signal
  For triangulation we only need about 4 of the strongest satellite codes
  To reduce the number of correlators we MF against a linear combination of all possibilities:
  Repeat several times with different combinations
Li, Rueetschi, Eldar and Scaglione, ’11

## Slide 128: Results
  MF requires 10,000 correlators
  Can meet performance with far fewer correlators
  Same idea applies to multi-user detection
  (Xie, Eldar and Goldsmith, 10)

## Slide 129
Xampling Systems
Eldar, ‘09
Vetterli et al., ’02-’07
Dragotti et al., ’02-’07
Gedalyahu, Tur and Eldar, ’10-’11
Tropp et al., ’09
Modulated wideband converter
Periodic nonuniform sampling (fully-blind)
Sparse shift-invariant framework
Finite rate of innovation sampling
Random demodulation
Mishali and Eldar, ‘07-’09
Mishali and Eldar, ‘07-’09

## Slide 130: Random Demodulation
Tropp et al., ‘09
Model: sparse sum of harmonic tones
Sampling:
Nyquist-rate

## Slide 131: Random Demodulation
Reconstruction:
Nyquist-rate
Use CS solvers to recover , then reconstruct
Numerical simulations: 32 kHz AM signal recovered from sampling
at 10% Nyquist rate
Tropp et al., ‘09
Similar to MWC? Next part describes the differences…

## Slide 132: Nyquist Folding
Lowpass
Rate reduction using nonlinear sampling effects:
Chart: 
Chart: 
Fudge et al., ‘08

## Slide 133: Summary: Xampling Systems
X-DSP | X-ADC | Strategy |  | Model
CTF | Periodic mixing | MWC Mishali-Eldar 09 |  | Multiband
CTF | time shifts | PNS Mishali-Eldar 08 |  | 
 | Jittered undersampling | Nyquist-folding Fudge et al. 08 |  | 
CTF | Filter-bank | Eldar 08 |  | Sparse shift-invariant
Annihilating filter | Lowpass | Periodic Vetterli et al. 02-05 |  | FRI (time-delays)
Moments factoring | Splines | One-shot Dragotti et al. 07 |  | 
Annihilating filter | Sum-of-Sincs filtering | Periodic/one-shot Gedlyahu-Tur-Eldar 09-10 |  | 
MUSIC or ESPRIT | Lowpass or periodic mixing + integration | Gadlyahu-Eldar 09 |  | Sequences of innovation
CS | Sign flipping + integration | RD Tropp et al. 09 |  | Harmonic tones
``Xampling: Signal Acquisition and Processing in Union of Subspaces’’, Mishali, Eldar and Elron, TSP ‘11

## Slide 134
– Part 5 –
From Theory to Hardware
 Outline

## Slide 135: Theory vs. Practice
Practical considerations affect the choice of a sampling solution
Example 1: Multiband sampling (known carriers )
Example 1: Pulse streams (known delays )
 | RF demodulation | Nonuniform methods
Minimal analog preprocessing |  | 
ADC with low analog bandwidth |  | 
 |  | Digital match filter
Low sampling rate |  | 
Robustness to model mismatch |  | 


## Slide 136: ADC Market
State-of-the-art ADCs generate Nyquist samples
Today’s challenges:
  Increase sampling rate (Giga-samples/sec)
  Increase front-end bandwidth
  Increase (effective) number of bits

## Slide 137: Sub-Nyquist: Practical Challenges
Goal: Shift challenge away from ADC technology
No free lunches ! Signal has frequencies until
Nyquist will enter elsewhere into system design
Practical design metrics:
  robustness to model mismatches
  flexible hardware design
  light computational loads
  imaging: high resolution
  noise performance
  power, area, size, cost, …
Next slides:
  Study practical metrics of example sub-Nyquist systems (RD/MWC)
  Glance into sub-Nyquist circuit challenges
  Sub-Nyquist imaging: analog vs. discrete CS
Focus of this part

## Slide 138: Random Demodulator
Robustness:
0.005% grid mismatch
Required hardware accuracy (so that ):
Accurate integrator:
Computational load:
Reported hardware:
``Nice’’
time-domain
appearance
Tropp et al., ‘09
Ragheb et al., ‘08
Yu et al., ‘10

## Slide 139: Modulated Wideband Converter
Robustness:
Mishali and Eldar, ‘09
Inequalities allow model mismatches
Required hardware accuracy:
``Nice’’
freq.-domain
appearance
Nonideal lowpass response can be compensated digitally
Chen et al., ‘10
Computational load:
Reported hardware:
Mishali et al., ‘11

## Slide 140: Hardware Accuracy
Sign alternating functions at 2 GHz rate
Time appearance
Frequency appearance

## Slide 141: Comparison
Tropp et al., ‘09
Mishali and Eldar, ‘09
Visually-similar systems – major differences in practical metrics
  Time-domain accuracy
  Computational loads
  Freq.-domain accuracy
  (handled by RF front-end)
No free lunches… Nyquist enters in:
Similar conclusions in other applications?

## Slide 142: CS Radar
A discrete version of the channel is being estimated
Leakage effect  fake targets
Limited resolution to
Sampling process in hardware is unclear
Digital processing is complex and expensive
Leakage effect  fake targets
Real channel
Discretized channel
Notes: Moshiko: add ref to the graphs

## Slide 143: ADCs: Why Not Standard CS?
CS is for finite dimensional models (y=Ax)
Loss in resolution when discretizing
Sensitivity to grid, analog bandwidth issues
Is not able to exploit structure in analog signals
Results in large computation on the digital side
Samples do not typically interface with standard processing methods
Besides union models and Xampling there are many more challenges !
More details in: M. Mishali, Y. C. Eldar, and A. Elron, “Xampling: Signal acquisition and processing in union of subspaces”

## Slide 144: Stepping CS to Practice
Address wideband noise and dynamic range:
  Since x is noisy: y=A(x+e)+w, e=wideband noise
  MWC/PNS: Nyquist-bandwidth noise is aliased
  RD: noise is folded from all possible tone locations
  Large interference will swamp ADC
Integrate into existing systems
  Minimal (preferably no) modification to hardware
  e.g., reprogramming firmware, rewiring, etc.
  Deal with large analog BW and wide dynamic range
Prove cost-effective
  Rate is only one factor ! Digital complexity is not less important
  Improve effective number of bits / Xample
Next slides: quick glance at circuit challenges + applications

## Slide 145: A 2.4 GHz Prototype
2.3 GHz Nyquist-rate, 120 MHz occupancy
280 MHz sampling rate
Wideband receiver mode:
  49 dB dynamic range
  SNDR > 30 dB over all input range
ADC mode:
  1.2 volt peak-to-peak full-scale
  42 dB SNDR = 6.7 ENOB
Off-the-shelf devices, ~5k$, standard PCB production
Mishali and Eldar, ’08-10

## Slide 146: Circuit Design (2)
Analog board
  m=4 channels
  1:4 Split + mixing + filtering
  Filter cutoff 33 MHz
  Sampling rate 70 MHz per channel (scope)
Digital board: sign alternating sequences
  2.075 GHz VCO
  Discrete ECL shift-register
  M=108 bits
  4 Outputs (taps of the register)
Mishali and Eldar, ’08-10

## Slide 147: Circuit Design (3)
Wideband receiver mode:
  Gain control on the input
  Design specifications:
  Power out > -7 dBm
  SNDR > 30 dB
  over all input range
  Gives 49 dB dynamic range
Mishali and Eldar, ’08-10

## Slide 148: Analog Design
Mishali et al., ‘10

## Slide 149: Digital Design
Mishali et al., ‘10

## Slide 150: Mixing with Periodic Functions
support wideband LO
Cannot equalize
entire path
Fine biasing due to sinusoids power split
Datasheet specifications are for single LO mixing (conversion loss, IP3, required power) !
Mishali et al., ’10

## Slide 151: Highly-Transient Periodic Waveforms
We selected the sign pattern which gives about the same harmonic levels
Tap locations: 5th bit in every consecutive 24 bits (layout considerations only)
Mishali et al., ‘10

## Slide 152: Sub-Nyquist Demonstration
FM @ 631.2 MHz
AM @ 807.8 MHz
1.5 MHz
10 kHz
100 kHz
Overlayed sub-Nyquist
aliasing around 6.171 MHz
+
+
FM @ 631.2 MHz
AM @ 807.8 MHz
Sine @ 981.9 MHz
MWC prototype
Carrier frequencies are chosen to create overlayed aliasing at baseband
Reconstruction
(CTF)
Mishali et al., ‘10

## Slide 153: Application: Cognitive Radio
~
~
~
~
hole
hole
Sub-Nyquist sampling
Xampling for Spectrum Sensing
Detect active
spectrum slices
Fine support
detection
For example:
Mishali and Eldar, ’11
Notes: Emphasize that this is a degenerated version of the MWC for the task of spectrum sensing

## Slide 154: Simulations
3 QPSK transmissions, Symbol rate = 30 MHz,
Quality measure, CFO = Carrier frequency offset
Satisfies IEEE 802.11 40ppm specifications of standard transmissions around 3.75 GHz
Mishali and Eldar, ’11
Notes: In the simulations we used 3 QPSK signals
The carriers, bits, energy etc were all drawn randomly. However, emphasize that the system parameters were fixed (no random in the operator)
As can be seen > 99% of the simulations (100 trials X 3 transmission = 300) were within 150 kHz, this was done for SNR=15 dB
For other SNR values and other CFO_max (30/70/100/200 kHz) the second plot shows a graceful behavior

## Slide 155: Experiments
Mishali and Eldar, ’11

## Slide 156: Take-Home Message
Compressed sensing uses finite models
Xampling works for analog signals
Compression
Sampling
Must combine ideas from Sampling theory and algorithms from CS
  CS+Sampling = Xampling
X prefix for compression, e.g. DivX

## Slide 157: Summary: Next Big Challenge
Develop cost-effective CS hardware solutions
Address wideband noise and dynamic range
Integrate into existing hardware solutions
Innovate at the circuit level: wideband input and large dynamic range
Design provable hardware
  at lab
  on-board
  on-chip
Become a mature technology !

## Slide 158
Conclusions
Q & A
 Outline

## Slide 159
Union of subspaces: broad and flexible model
Can lead to simple and efficient algorithms
Includes analog signal models
Sub-Nyquist sampler in hardware
Compressed sensing of many classes of analog signals
Many research opportunities: extensions, robustness, hardware, mathematical …
Compressed sensing can be extended practically to the infinite analog domain!
Conclusions

## Slide 160
Burst of innovative publications
Theory is still developing, yet the basic principles are understood
Next frontier: Hardware implementations
Become a mature technology !
Opinion
More details in:
M. Mishali and Y. C. Eldar, “Sub-Nyquist Sampling: Bridging Theory and Practice,’’ Sig. Proc. Mag.
M. Duarte and Y. C. Eldar, “Structured Compressed Sensing: From Theory to Applications,” TSP.
M. Mishali and Y. C. Eldar, “Xampling: Compressed Sensing of Analog Signals,’’ in book, Cambridge press.

## Slide 161
References + Online Documentations
 Outline

## Slide 162: Online Demonstrations
GUI package of the MWC
Video recording of sub-Nyquist sampling + carrier recovery in lab
SiPS 2010
2010 IEEE Workshop on
Signal Processing Systems

## Slide 163: Xampling Website
webee.technion.ac.il/people/YoninaEldar/xampling_top.html

## Slide 164
Acknowledgements
Thank you!
We’ll be happy to hear your comments, ideas for future work etc yonina@ee.technion.ac.il
Kfir Gedalyahu
Ronen Tur
Moshe Mishali
Students:
Collaborators:
Noam Wagner
General Electric Israel – Zvi Friedman
National Instruments Corp. – Ahsan Aziz, Sam Shearman, Eran Castiel
Sponsors:
Newcom Network of Excellence
Israel Science Foundation
Magneton

## Slide 165: References
Tutorials:
M. Mishali and Y. C. Eldar, “Sub-Nyquist Sampling: Bridging Theory and Practice,’’ IEEE Sig. Proc. Mag.
M. Duarte and Y. C. Eldar, “Structured Compressed Sensing: From Theory to Applications,” TSP
M. Mishali and Y. C. Eldar, “Xampling: Compressed Sensing of Analog Signals,’’ in book, Cambridge press
Y. C. Eldar and G. Kutyniok, “Compressed Sensing: Theory and Applications,” Cambridge Press
Other Tutorials and Summaries:
R. G. Baraniuk, “Compressive sensing,” IEEE Sig. Proc. Mag., vol. 24, no. 4, pp. 118–120, 124, July 2007
E. J. Candès and M. B. Wakin, “An introduction to compressive sampling,” IEEE Sig. Proc. Mag., vol. 25, pp. 21–30, Mar. 2008
J. Uriguen, Y. C. Eldar, P. L. Dragotti and Z. Ben-Haim, "Sampling at the Rate of Innovation: Theory and Applications,’’ in book, Cambridge press

## Slide 166: References
Generalized Sampling Theory:
A. J. Jerry, “The Shannon sampling theorem-Its various extensions and applications: A tutorial review,” Proc. Of the IEEE, vol. 65, no. 11, pp. 1565-1596, Nov. 1977
A. Aldroubi and M. Unser, “Sampling procedures in function spaces and asymptotic equivalence with Shannon’s sampling theory,” Numer. Funct. Anal. Optimiz., vol. 15, pp. 1-21, Feb. 1994
M. Unser and A. Aldroubi, “A general sampling theory for nonideal acquisition devices, “IEEE Trans. Signal Process., vol. 42, no. 11, pp. 2915-2925, Nov. 1994
C. de Boor, R. DeVore and A. Ron, “The structure of finitely generated shift-invariant spaces in ,” J. Funct. Anal, vol. 119, no. 1, pp. 37-78, 1994
A. Aldroubi, “Oblique projections in atomic spaces,” Proc. Amer. Math. Soc. , vol. 124, no. 7, pp. 2051-2060, 1996
M. Unser, “Sampling – 50 years after Shannon,” IEEE Proc., vol. 88, pp. 569-587, Apr. 2000
P. P. Vaidyanathan, “Generalizations of the sampling theorem: Seven decades after Nyquist,” IEEE Trans. Circuit Syst. I, vol. 48, no. 9, pp. 1094-1109, Sep. 2001
Y. C. Eldar and T. Michaeli, “Beyond bandlimited sampling,” IEEE Signal Process. Mag., vol. 26, no. 3, pp.
48–68, May 2009.
T. Michaeli and Y. C. Eldar, “Optimization Techniques in Modern Sampling Theory, ” in book Cambridge Univ. Press, ch., pp. 266–314, 2010

## Slide 167: References
Subspace Sampling:
I. Djokovic and P. P. Vaidyanathan, “Generalized sampling theorem in multiresolution subspaces,” IEEE Trans. Signal Process. , vol. 45, pp. 583-599, Mar. 1997
M. Unser, “Splines: A perfect fit for signal and image processing,” IEEE Signal Process. Mag., pp. 22-38, Nov. 1999
Y. C. Eldar and A. V. Oppenheim, “Filter bank reconstruction of bandlimited signals from nonuniform and generalized samples,” IEEE Trans. Signal Processing, vol. 48, no. 10, pp. 2864-2875, 2000
A. Aldroubi and K. Gröchenig, “Non-uniform sampling and reconstruction in shift-invariant spaces,” SIAM Review, vol. 43, pp. 585-620, 2001
Y. C. Eldar, “Sampling and reconstruction in arbitrary spaces and oblique dual frame vectors,” J. Fourier Analys. Appl., vol. 1, no. 9, pp. 77-96, Jan. 2003
O. Christensen and Y. C. Eldar, “Oblique dual frames and shift-invariant spaces,” Applied and Computational Harmonic Analysis, vol. 17, no. 1, pp. 48-68, Jul. 2004
O. Christensen and Y. C. Eldar, “Generalized shift-invariant systems and frames for subspaces,” J. Fourier Analys. Appl., vol. 11, pp. 299-313, 2005
Y. C. Eldar and T. Werther, “General framework for consistent sampling in Hilbert spaces,” International Journal of Wavelets, Multiresolution, and Information Processing, vol. 3, no. 3, pp. 347-359, Sep. 2005
Y. C. Eldar and O. Christensen, “Caracterization of Oblique Dual Frame Pairs,” J. Applied Signal Processing, vol. 2006, Article ID 92674, pp. 1-11
T. G. Dvorkind, Y. C. Eldar and E. Matusiak, “Nonlinear and non-ideal sampling: Theory and methods,” IEEE Trans. Signal Processing, vol. 56, no. 12, pp. 5874-5890, Dec. 2008

## Slide 168: References
Multiband subspaces:
H. J. Landau, “Necessary density conditions for sampling and interpolation of certain entire functions,” Acta Math., vol. 117, pp. 37-52, Feb. 1967
A. Kohlenberg, “Exact interpolation of band-limited functions,” J. Appl. Phys., pp. 1432–1435, Dec. 1953
R. G. Vaughan, N. L. Scott, and D. R. White, “The theory of bandpass sampling,” IEEE Trans. Signal Process., vol. 39, no. 9, pp. 1973–1984, Sep. 1991
Y.-P. Lin and P. P. Vaidyanathan, “Periodically nonuniform sampling of bandpass signals,” IEEE Trans. Circuits Syst. II, vol. 45, no. 3, pp. 340-351, Mar. 1998
C. Herley and P. W. Wong, “Minimum rate sampling and reconstruction of signals with arbitrary frequency support,” IEEE Trans. Inform. Theory, vol. 45, no. 5, pp. 1555-1564, Jul. 1999
R. Venkataramani and Y. Bresler, “Perfect reconstruction formulas and bounds on aliasing error in sub-Nyquist nonuniform sampling of multiband signals,” IEEE Trans. Inf. Theory, vol. 46, no. 6, pp. 2173–2183, Sep. 2000

## Slide 169: References
Union of Subspaces:
Y. M. Lu and M. N. Do, “A theory for sampling signals from a union of subspaces,” IEEE Trans. Signal Processing, vol. 56, no. 6, pp. 2334–2345, 2008
Y. C. Eldar and M. Mishali, “Robust recovery of signals from a structured union of subspaces,” IEEE Trans. Info. Theory, vol. 55, no. 11, pp. 5302–5316, 2009
T. Blumensath and M. E. Davies, “Sampling theorems for signals from the union of finite-dimensional linear subspaces,” IEEE Trans. Inf. Theory, vol. 55, no. 4, pp. 1872–1882, Apr. 2009
Xampling Framework:
Y. C. Eldar, “Compressed sensing of analog signals in shift-invariant spaces”, IEEE Trans. Signal Processing, vol. 57, no. 8, pp. 2986-2997, August 2009
Y. C. Eldar, “Uncertainty relations for analog signals,” IEEE Trans. Inform. Theory, vol. 55, no. 12, pp. 5742 - 5757, Dec. 2009
M. Mishali, Y. C. Eldar, and A. Elron, “Xampling: Signal acquisition and processing in union of subspaces,” [Online] arXiv.org 0911.0519, Oct. 2009
M. Mishali, Y. C. Eldar, O. Dounaevsky, and E. Shoshan, “Xampling: Analog to digital at sub-Nyquist rates,” IET Circuits, Devices & Systems, vol. 5, no. 1, pp. 8–20, Jan. 2011

## Slide 170: References
Modulated Wideband Converter / Fully-blind Multi-Coset:
M. Mishali and Y. C. Eldar, “Blind multiband signal reconstruction: Compressed sensing for analog signals,” IEEE Trans. Signal Processing, vol. 57, pp. 993–1009, Mar. 2009
M. Mishali and Y. C. Eldar, “From theory to practice: Sub-Nyquist sampling of sparse wideband analog signals,” IEEE Journal of Selected Topics on Signal Processing, vol. 4, pp. 375-391, April 2010
M. Mishali, Y. C. Eldar, O. Dounaevsky, and E. Shoshan, “Xampling: Analog to digital at sub-nyquist rates,” IET Circuits, Devices and Systems, vol. 5, no. 1, pp. 8–20, Jan. 2011
M. Mishali and Y. C. Eldar, “Reduce and boost: Recovering arbitrary sets of jointly sparse vectors,” IEEE Trans. Signal Processing, vol. 56, no. 10, pp. 4692–4702, Oct. 2008
M. Mishali and Y. C. Eldar, “Wideband spectrum sensing at sub-Nyquist rates,” to appear in IEEE Signal Process. Mag.; [Online] arXiv.org 1009.1305, Sep. 2010
Random Demodulator:
J. A. Tropp, J. N. Laska, M. F. Duarte, J. K. Romberg, and R. G. Baraniuk, “Beyond Nyquist: Efficient sampling of sparse bandlimited signals,” IEEE Trans. Inf. Theory, vol. 56, no. 1, pp. 520–544, Jan. 2010
Z. Yu, S. Hoyos, and B. M. Sadler, “Mixed-signal parallel compressed sensing and reception for cognitive radio,” in ICASSP, 2008, pp. 3861–3864
T. Ragheb, J. N. Laska, H. Nejati, S. Kirolos, R. G. Baraniuk, and Y. Massoud, “A prototype hardware for random demodulation based compressive analog-to-digital conversion,” in Circuits and Systems, 2008. MWSCAS 2008. 51st Midwest Symposium on, 2008, pp. 37–40
Z. Yu, X. Chen, S. Hoyos, B. M. Sadler, J. Gong, and C. Qian, “Mixed-signal parallel compressive spectrum sensing for cognitive radios,” International Journal of Digital Multimedia Broadcasting, 2010

## Slide 171: References
Pulse streams:
M. Vetterli, P. Marziliano, and T. Blu, “Sampling signals with finite rate of innovation,” IEEE Trans. Signal Process., vol. 50, no. 6, pp. 1417–1428, 2002
P. L. Dragotti, M. Vetterli, and T. Blu, “Sampling moments and reconstructing signals of finite rate of innovation: Shannon meets Strang Fix,” IEEE Trans. Signal Process., vol. 55, no. 5, pp. 1741–1757, May 2007
J. Kusuma and V. Goyal, “Multichannel sampling of parametric signals with a successive approximation property,” IEEE Int. Conf. Image Procesing (ICIP), pp. 1265–1268, Oct. 2006
C. Seelamantula and M. Unser, “A generalized sampling method for finite-rate-of-innovation-signal reconstruction,” IEEE Signal Process. Lett., vol. 15, pp. 813–816, 2008
E. Matusiak and Y. C. Eldar, “Sub-Nyquist sampling of short pulses: Theory,” [Online] arXiv.org 1010.3132
Z. Ben-Haim, T. Michaeli, and Y. C. Eldar, “Performance bounds and design criteria for estimating finite rate of innovation signals,” [Online] arXiv.org 1009.2221, Sep. 2010
L. Baboulaz and P. L. Dragotti, “Exact feature extraction using finite rate of innovation principles with an
application to image super-resolution,” IEEE Trans. Image Process., vol. 18, no. 2, pp. 281–298, Feb. 2009
K. Gedalyahu and Y. C. Eldar, "Time-delay estimation from low-rate samples: A union of subspaces approach," IEEE Trans. Signal Processing, vol. 58, no. 6, pp. 3017–3031, June 2010
R. Tur, Y. C. Eldar, and Z. Friedman, “Innovation rate sampling of pulse streams with application to ultrasound imaging,” IEEE Trans. Signal Process., vol. 59, no. 4, pp. 1827–1842, Apr. 2011
K. Gedalyahu, R. Tur, and Y. C. Eldar, “Multichannel sampling of pulse streams at the rate of innovation,” IEEE Trans. Signal Process., vol. 59, no. 4, pp. 1491–1504, Apr. 2011
W. U. Bajwa, K. Gedalyahu, and Y. C. Eldar, “Identification of underspread linear systems with application to super-resolution radar,” to appear in IEEE Trans. Signal Processing

## Slide 172: References
Compressed sensing (#1):
D. L. Donoho, “Compressed sensing,” IEEE Trans. Info. Theory, vol. 52, no. 4, pp. 1289–1306, Sep. 2006
E. J. Candès, J. K. Romberg, and T. Tao, “Robust uncertainty principles: Exact signal reconstruction from highly incomplete frequency information,” IEEE Trans. Info. Theory, vol. 52, no. 2, pp. 489–509, 2006
E. J. Candès and T. Tao, “Near optimal signal recovery from random projections: Universal encoding strategies?,” IEEE Trans. Info. Theory, vol. 52, no. 12, pp. 5406–5425, Dec. 2006
J. A. Tropp, “Greed is good: Algorithmic results for sparse approximation,” IEEE Trans. Info. Theory, vol. 50, no. 10, pp. 2231–2242, Oct. 2004
D. Needell and J. A. Tropp, “CoSaMP: Iterative signal recovery from incomplete and inaccurate samples,” Appl. Comput. Harmon. Anal., vol. 26, no. 3, pp. 301–321, May 2008
J. A. Tropp, A. C. Gilbert, and M. J. Strauss, “Algorithms for simultaneous sparse approximation. Part I: Greedy pursuit,” Signal Processing, vol. 86, pp. 572–588, Apr. 2006
J. A. Tropp, “Algorithms for simultaneous sparse approximation. Part II: Convex relaxation,” Signal Processing, vol. 86, Apr. 2006
D. L. Donoho and M. Elad, “Optimally sparse representation in general (nonorthogonal) dictionaries via `1 minimization,” Proc. Nat. Acad. Sci., vol. 100, no. 5, pp. 2197–2202, Mar. 2003
Z. Ben-Haim and Y. C. Eldar, "The Cramér–Rao bound for estimating a sparse parameter vector," IEEE Trans. Signal Processing, vol. 58, no. 6, pp. 3384–3389, June 2010
I. F. Gorodnitsky and B. D. Rao, “Sparse signal reconstruction from limited data using FOCUSS: A re-weighted minimum norm algorithm,” IEEE Trans. Signal Processing, vol. 45, no. 3, pp. 600–616, Mar. 1997

## Slide 173: References
Compressed sensing (#2):
Z. Ben-Haim, Y. C. Eldar, and M. Elad, “Coherence-based performance guarantees for estimating a sparse vector under random noise,” IEEE Trans. Signal Processing, vol. 58, no. 10, pp. 5030–5043, Oct. 2010
S. F. Cotter, B. D. Rao, K. Engan, and K. Kreutz-Delgado, “Sparse solutions to linear inverse problems with multiple measurement vectors,” IEEE Trans. Signal Processing, vol. 53, no. 7, pp. 2477–2488, July 2005
J. Chen and X. Huo, “Theoretical results on sparse representations of multiple-measurement vectors,” IEEE Trans. Signal Processing, vol. 54, no. 12, pp. 4634–4643, Dec. 2006
M. Mishali and Y. C. Eldar, “Reduce and boost: Recovering arbitrary sets of jointly sparse vectors,” IEEE Trans. Signal Processing, vol. 56, no. 10, pp. 4692–4702, Oct. 2008
S. Mallat and Z. Zhang, “Matching pursuit with time-frequency dictionaries,” IEEE Trans. Signal Processing, vol. 41, no. 12, pp. 3397–3415, Dec. 1993
Y. Pati, R. Rezaifar, and P. Krishnaprasad, “Orthogonal matching pursuit: Recursive function approximation with applications to wavelet decomposition,” in Asilomar Conf. Signals, Systems, and Computers, Pacific Grove, CA, Nov. 1993
M. E. Davies and Y. C. Eldar, “Rank awareness in joint sparse recovery,” Apr. 2010, Preprint
D. Baron, M. B. Wakin, M. F. Duarte, S. Sarvotham, and R. G. Baraniuk, “Distributed compressed sensing,” Tech. Rep. TREE-0612, Rice University, Department of Electrical and Computer Engineering, Houston, TX, Nov. 2006

## Slide 174
Thank you